## Slide 1: Javad Lavaei Department of Electrical Engineering Columbia University Joint work with Somayeh Sojoudi
Convexification of Optimal Power Flow Problem by Means of Phase Shifters

## Slide 2: Power Networks
Optimizations:
  Optimal power flow (OPF)
  Security-constrained OPF
  State estimation
  Network reconfiguration
  Unit commitment
  Dynamic energy management
Issue of non-convexity:
  Discrete parameters
  Nonlinearity in continuous variables
Transition from traditional grid to smart grid:
  More variables (10X)
  Time constraints (100X)
Javad Lavaei, Columbia University
2

## Slide 3: Broad Interest in Optimal Power Flow
Javad Lavaei, Columbia University
3
OPF-based problems solved on different time scales:
  Electricity market
  Real-time operation
  Security assessment
  Transmission planning
Existing methods based on linearization or local search
Question: How to find the best solution using a scalable robust algorithm?
Huge literature since 1962 by power, OR and Econ people

## Slide 4: Summary of Results
Javad Lavaei, Columbia University
4
A sufficient condition to globally solve OPF:
  Numerous randomly generated systems
  IEEE systems with 14, 30, 57, 118, 300 buses
  European grid
Various theories: It holds widely in practice
Project 1: How to solve a given OPF in polynomial time? (joint work with Steven Low)
Distribution networks are fine (under certain assumptions).
Every transmission network can be turned into a good one (under assumptions).
Project 2: Find network topologies over which optimization is easy? (joint work with Somayeh Sojoudi, David Tse and Baosen Zhang)

## Slide 5: Summary of Results
Javad Lavaei, Columbia University
5
Project 3: How to design a distributed algorithm for solving OPF? (joint work with Stephen Boyd, Eric Chu and Matt Kranning)
A practical (infinitely) parallelizable algorithm
It solves 10,000-bus OPF in 0.85 seconds on a single core machine.
Project 4: How to do optimization for mesh networks? (joint work with Ramtin Madani and Somayeh Sojoudi)
Developed a penalization technique
Verified its performance on IEEE systems with 7000 cost functions
Focus of this talk: Revisit Project 2 and remove its assumptions

## Slide 6: Geometric Intuition: Two-Generator Network
Javad Lavaei, Columbia University
6

## Slide 7: Optimal Power Flow
Cost
Operation
Flow
Balance
SDP relaxation: Remove the rank constraint.
Exactness of relaxation: We study it thru a geometric approach.
Javad Lavaei, Columbia University
7

## Slide 8: Acyclic Three-Bus Networks
Assume that the voltage magnitude is fixed at every bus.
Javad Lavaei, Columbia University
8

## Slide 9: Geometric Interpretation
(+,+)
Pareto face:
Pareto face
Convex Pareto Front: Injection region and its convex hull share the same front.
Javad Lavaei, Columbia University
9

## Slide 10: Two-Bus Network
Two-bus network with power constraints:
P1
P2
P1
P2
P1
P2
P1
P2
P1
P2
P1
P2
Javad Lavaei, Columbia University
10

## Slide 11: General Tree Network
Assume that each flow-restricted region is already Pareto (monotonic curve):
Pij
Pji
Ratio from 1 to 10: Max angle from 45o to 80o
Javad Lavaei, Columbia University
11

## Slide 12: Three-Bus Networks
Issues: Coupling thru angles and voltage magnitudes
  Variable voltage magnitude:
Javad Lavaei, Columbia University
12

## Slide 13: Decoupling Angles
Phase shifter: An ideal transformer changing a phase
Phase shifter kills the angles coupling.
PS
Javad Lavaei, Columbia University
13

## Slide 14: Decoupling Voltage Magnitudes
Define:
Boundary
Javad Lavaei, Columbia University
14

## Slide 15: Injection & Flow Regions
Voltage coupling introduces linear
equations in a high-dimensional space.
Line (i,j):
Javad Lavaei, Columbia University
15

## Slide 16: Main Result
Current practice in power systems:
  Tight voltage magnitudes.
  Not too large angle differences.
Adding virtual phase shifters is often the only relaxation needed in practice.
Javad Lavaei, Columbia University
16

## Slide 17: Phase Shifters
Javad Lavaei, Columbia University
17
Blue: Feasible set (PG1,PG2)
Green: Effect of phase shifter
Red: Effect of convexification
Minimization over green = Minimization over green and red (even with box constraints)

## Slide 18: Phase Shifters
Simulations:
  Zero duality gap for IEEE 30-bus system
  Guarantee zero duality gap for all possible load profiles?
  Theoretical side: Add 12 phase shifters
  Practical side: 2 phase shifters are enough
  IEEE 118-bus system needs no phase shifters (power loss case)
Javad Lavaei, Columbia University
18
Phase shifters speed up the computation:

## Slide 19: Conclusions
Focus: OPF with a 50-year history
Goal: Find a near-global solution efficiently
Main result: Virtual phase shifters make OPF easy under tight voltage magnitudes and not too loose angle differences.
Future work: How to lessen the effect of virtual phase shifters?
Javad Lavaei, Columbia University
19