## Slide 1: Javad Lavaei Department of Electrical Engineering Columbia University
An Efficient Computational Method for Large-Scale Operations Planning in Power Systems

## Slide 2
Acknowledgements
Caltech: Steven Low, Somayeh Sojoudi
Columbia University: Ramtin Madani
UC Berkeley: David Tse, Baosen Zhang
Stanford University: Stephen Boyd, Eric Chu, Matt Kranning
J. Lavaei and S. Low, "Zero Duality Gap in Optimal Power Flow Problem," IEEE Transactions on Power Systems, 2012.
J. Lavaei, D. Tse and B. Zhang, "Geometry of Power Flows in Tree Networks,“ in IEEE Power & Energy Society General Meeting, 2012.
S. Sojoudi and J. Lavaei, "Physics of Power Networks Makes Hard Optimization Problems Easy To Solve,“ in IEEE Power & Energy Society General Meeting, 2012.
M. Kraning, E. Chu, J. Lavaei and S. Boyd, "Message Passing for Dynamic Network Energy Management," Submitted for publication, 2012.
S. Sojoudi and J. Lavaei, "Semidefinite Relaxation for Nonlinear Optimization over Graphs with Application to Optimal Power Flow Problem," Working draft, 2012.
S. Sojoudi and J. Lavaei, "Convexification of Generalized Network Flow Problem with Application to Optimal Power Flow," Working draft, 2012.

## Slide 3: Power Networks (CDC 10, Allerton 10, ACC 11, TPS 11, ACC 12, PGM 12)
Optimizations:
  Resource allocation
  State estimation
  Scheduling
Issue: Nonlinearities
(power quadratic in voltage)
Transition from traditional grid to smart grid:
  More variables (10X)
  Time constraints (100X)
Javad Lavaei, Columbia University
3

## Slide 4: Resource Allocation: Optimal Power Flow (OPF)
Javad Lavaei, Columbia University
4
OPF: Given constant-power loads, find optimal P’s subject to:
  Demand constraints
  Constraints on V’s, P’s, and Q’s.
Voltage V
Complex power = VI*=P + Q i
Current I

## Slide 5: Broad Interest in Optimal Power Flow
Javad Lavaei, Columbia University
5
Interested companies: ISOs, TSOs, RTOs, Utilities, FERC
OPF solved on different time scales:
  Electricity market
  Real-time operation
  Security assessment
  Transmission planning
Existing methods based on linearization or local search
Can save $$$ if solved efficiently
Huge literature since 1962 by power, OR and Econ people
Recent conference by Federal Energy Regulatory Commission about OPF

## Slide 6: Local Solutions
Javad Lavaei, Columbia University
6
Local solution: $1502 Global solution: $338
OPF
P1
P2

## Slide 7: Local Solutions
Anya Castillo et al.
Ian Hiskens from Umich:
Source of Difficulty: Power is quadratic in terms of complex voltages.
Study of local solutions by Edinburgh’s group
Javad Lavaei, Columbia University
7

## Slide 8: Summary of Results
Javad Lavaei, Columbia University
8
A sufficient condition to globally solve OPF:
  Numerous randomly generated systems
  IEEE systems with 14, 30, 57, 118, 300 buses
  European grid
Various theories: It holds widely in practice
Project 1: How to solve a given OPF in polynomial time? (joint work with Steven Low)
Distribution networks are fine.
Every transmission network can be turned into a good one.
Project 2: Find network topologies over which optimization is easy? (joint work with Somayeh Sojoudi, David Tse and Baosen Zhang)

## Slide 9: Summary of Results
Javad Lavaei, Columbia University
9
Project 3: How to design a distributed algorithm for solving OPF? (joint work with Stephen Boyd, Eric Chu and Matt Kranning)
A practical (infinitely) parallelizable algorithm
It solves 10,000-bus OPF in 0.85 seconds on a single core machine.
Project 5: How to relate the polynomial-time solvability of an optimization to its structural properties? (joint work with Somayeh Sojoudi)
Project 6: How to solve generalized network flow (CS problem)? (joint work with Somayeh Sojoudi)
Project 4: How to do optimization for mesh networks? (joint work with Ramtin Madani)

## Slide 10: Geometric Intuition: Two-Generator Network
Javad Lavaei, Columbia University
10

## Slide 11: Optimal Power Flow
Cost
Operation
Flow
Balance
Extensions:
  Other objective (voltage support, reactive power, deviation)
  More variables, e.g. capacitor banks, transformers
  Preventive or corrective contingency constraints
  Multi-period OPF
Conventional OPF captures common sources of non-convexity.
Javad Lavaei, Columbia University
11

## Slide 12: Optimal Power Flow
Express balance equations as inequalities:
Proof without this change involves geometric techniques.
Allow power over-delivery or assume positive LMPs.
Javad Lavaei, Columbia University
12

## Slide 13: Various Relaxations
Dual OPF
SDP
OPF
R-SDP
SOCP
Javad Lavaei, Columbia University
13
SDP relaxation has a rank-one solution for:
  IEEE systems with 14, 30, 57, 118, 300 buses
  European grid
Exactness of SDP relaxation and zero duality gap are equivalent for OPF.

## Slide 14: Zero Duality Gap
Networks:
  Distribution (acyclic)
  Transmission (cyclic)
OPF:
  Real-valued (DC)
  Complex-valued (AC)
DC lines are becoming more deployed (Nordic circuit).
Theory applies to scheduling of EVs charging, control of PV invertors,...
Javad Lavaei, Columbia University
14

## Slide 15: AC Transmission Networks
How about AC transmission networks?
  May not be true for every network
  Various sufficient conditions
Result 1: AC transmission network manipulation:
  High performance (lower generation cost)
  Easy optimization
  Easy market (positive LMPs and existence of eq. pt.)
Result 2: Reduced computational complexity
Bus-4
Bus-2
Bus-3
Bus-5
Bus-1
PS
Javad Lavaei, Columbia University
15

## Slide 16: Simulations
Simulations:
  Zero duality gap for IEEE 30-bus system
  Guarantee zero duality gap for all possible load profiles?
  Theoretical side: Add 12 phase shifters
  Practical side: 2 phase shifters are enough
  IEEE 118-bus system needs no phase shifters (power loss case)
Javad Lavaei, Columbia University
16

## Slide 17: OPF With Equality Constraints
Javad Lavaei, Columbia University
17
Injection region under fixed voltage magnitudes:
When can we allow equality constraints? Need to study Pareto front

## Slide 18: Convexification in Polar Coordinates
Javad Lavaei, Columbia University
18
Imposed implicitly (thermal, stability, etc.)
Imposed explicitly in the algorithm
Similar to the condition derived in Ross Baldick’s book

## Slide 19: Convexification in Polar Coordinates
Javad Lavaei, Columbia University
19
Idea:
Algorithm:
  Fix magnitudes and optimize phases
  Fix phases and optimize magnitudes

## Slide 20: Convexification in Polar Coordinates
Javad Lavaei, Columbia University
20
Can we jointly optimize phases and magnitudes?
Observation 1: Bounding |Vi| is the same as bounding Xi.
Observation 2: is convex for a large enough m.
Observation 3: is convex for a large enough m.
Observation 4: |Vi|2 is convex for m ≤ 2.
Change of variables:
Assumption (implicit or explicit):

## Slide 21: Lossy Networks
Javad Lavaei, Stanford University
17
Javad Lavaei, Columbia University
21
Assumption (implicit or explicit):
Conjecture: This assumptions leads to convexification in rectangular coordinates
(partially proved).
Relationship between polar and rectangular?

## Slide 22: Lossless Networks
Javad Lavaei, Stanford University
17
Javad Lavaei, Columbia University
22
(P1,P2)
(P12,P23,P31)
Lossless 3 bus
Consider a lossless AC transmission network.
SDP does not work well on lossless networks.

## Slide 23: Lossless Networks
Javad Lavaei, Stanford University
17
Javad Lavaei, Columbia University
23
Solution: Penalize the rank constraint in the objective:
Simulation for a 10-bus cycle:
  1) W has 8 nonzero eigs, but the regularization kills 7 of all (zero duality gap).
  2) This regularization is guaranteed to kill all but 1-2 eigs.
  3) Randomized “M” gives us the correct answer (nonzero duality gap).

## Slide 24: Conclusions
Focus: OPF with a 50-year history
Goal: Find a global solution efficiently
Obtained provably global solutions for many practical OPFs
Developed various theories for distribution and transmission networks
Several companies working on these ideas
Javad Lavaei, Columbia University
24